## Slide 1: ELec3300 Final demo
Auto Drawing Machine
Group 50 DU Yinwei, CHEN Yi

## Slide 2: Overview
Mechanical Design
Electronic Design
Software Design
Demo:
  Manual Mode: Touch and Bluetooth
  Camera Mode: Take a picture and send to laptop
  SD-Card Drawing Mode: Draw picture from SD card file
Reflection and Potential Improvement
Q&A

## Slide 3: Mechanical Design
2 Nema 17 stepper motor
SG90 sever motor

## Slide 4: Mechanical Design
How does it move?
In X axis, both motor move in same direction.
In Y axis, both motor move in opposite direction.

## Slide 5: Electronic Design
OV7725 Camera
USB to computer
LCD display and Touchscreen
Driver for stepper motor
HC05 Bluetooth
SD Card

## Slide 6: Software Design
Grayscale
Halftone
Pen path

## Slide 7: Software Design
Core Function:
  Read x, y offsets and move in a slash line
Problem:
  Two stepper motors are not independent
Solution:
  Motor_Move_XY(int x, int y)
  Motor 1 moves (x+y) steps, Motor 2 moves (x-y) steps.
  Set the speed of the two motors to be (x+y)/(x-y)
  However, the speed has limit (650-3500)  need appoximation

## Slide 8: Software design
Main Menu
Camera Mode
Bluetooth
USB Mode
SD card acts as a USB device to computer
Manual Mode
Display Image and capture screen
Receive and send instructions through phones
Touch
Touch the screen and move the pen
SD Card Mode
Choose the file you want to draw

## Slide 9: Demo
Camera Mode
  See the live capture of the camera
  Take a photo
USB Mode:
  Send the taken picture to computer via USB connection

## Slide 10: DEMO
Manual Mode
  Control by touch
  Control by Bluetooth

## Slide 11: Demo
Draw the picture from SD Card
  The picture will also be displayed on the screen

## Slide 12: Reflection
Engineering is sometimes way more than theory.
Get the crucial point first.
Think before try && try before think
ELEC is fun :)

## Slide 13: Improvement
Using G-code to make the drawing more powerful
Write an app(with GUI) so that we can make the control more friendly.

## Slide 14: Question?